## Slide 1: Aircraft oxygen systems
By: Phil Clay

## Slide 2: Introduction
Background
  Hypoxia Video
Oxygen Rules (FAR)
Non-OBOGS (On-board Oxygen Generating System) Oxygen Systems
OBOGS, and science behind it
Case study

## Slide 3: Background
As altitude increases, percent of oxygen in the air decreases
Time of Useful Consciousness (TUC)
Altitude (thousands of feet) | Time of useful consciousness
15 | 30 minutes or more
18 | 20-30 minutes
22 | 5-10 minutes
25 | 2-3 minutes
28 | 2.5-3 minutes
30 | 1-3 minutes
35 | 30-60 seconds
40 | 15-20 seconds
45 | 9-15 seconds
50 | 6-9 seconds

## Slide 4: Hypoxia example
https://www.youtube.com/watch?v=UN3W4d-5RPo
Dr. O’Neill’s addendum: https://youtu.be/OmeJlewaU7s
  Training systems are critical aircraft systems
  The training systems for the future T-X program is strongly stressed in the USAF requirements.
  If you are a civilian pilot, you should find a local FAA training facility and do a hypoxia chamber test…

## Slide 5: Oxygen Rules
FAR 91.211
  Above 12,500’ for more than 30 mins
  Above 14,000’
  Above 15,000’
  Pressurized above 25,000’
  Pressurized above 35,000’

## Slide 6: System types
5 different systems
  Continuous Flow
  Altitude Adjustable
  Altitude Compensating
  Demand
  Pressure-Demand

## Slide 7: Non-OBOgs oxygen systems

## Slide 8: Non obogs oxygen systems drawbacks
Expensive
Potentially dangerous
Takes up a lot of space to store the oxygen
Time limited

## Slide 9: Obogs (on board oxygen generating system)
Positives
  Compact
  Unlimited
  Very little maintenance
  Lowest cost
  Gas purity
Negatives
  Without bleed air, cannot fuction
  Can potentially drain battery

## Slide 10: Science behind Obogs
High pressure air from turbine
  3rd stage of compression in the T-6
Pressure swing absorbtion
  Zeolites
  High pressure vs. Low pressure

## Slide 11: Aircraft with OBOGS
F-35
T-6
B-1
B-2
F-18
Many more…

## Slide 12: Case study
Payne Stewart Crash
  October 25th ,1999

## Slide 13: Case Study
ValuJet Flight 592

## Slide 14: Background
Company founded in 1992
  Known for cost cutting measures
Very little training provided to workers
Maintenance performed by contractors

## Slide 15: Flight 592
Scheduled from Miami, FL to Atlanta, GA on 11 May, 1996 (DC-9)
  105 Passengers
  5 crew
20 minutes after take-off, smoke begins to fill passenger cabin
31 minutes into the flight, the aircraft impacted the ground in the everglades killing all on board

## Slide 16: NTSB Findings
Chemical Oxygen generators in cargo hold caught fire
Shortly before Take-off, boxes of “empty” oxygen bottles loaded into cargo hold
  Improperly boxed/packaged
Loud bang on CVR when smoke starts filling the cabin
NTSB report places responsibility for accident on three parties:
  SabreTech
  ValuJet
  FAA

## Slide 17: Summary
Background
Oxygen Rules (FAR)
Non-OBOGS Oxygen Systems
OBOGS, and the science behind it
Case study

## Slide 18: Sources
Wikipedia
  https://en.wikipedia.org/wiki/Time_of_useful_consciousness
AOPA Website
  http://www.aopa.org/Pilot-Resources/PIC-archive/Pilot-and-Passenger-Physiology/Oxygen-Use-in-Aviation
Honeywell Life support systems pamphlet

## Slide 19: Questions?
pmclay@crimson.ua.edu