## Slide 1: Engine Failure in Multiengine Aircraft
Mike Poremba
Aircraft Systems

## Slide 2: Outline
Who I Am
VMC
  What is VMC
  Why is VMC important
  VMC Correction
Engine Failure in Small Multiengine Aircraft
  Piper Seminole Engine Systems
Engine Failure in Larger Multiengine Aircraft
  Gulfstream G450
  Boeing 737
Case Study 1: TransAsia Flight 235
Case Study 2: Delta Airlines Flight 295

## Slide 3: Who I am
Graduate Student
  MS Aerospace Engineering
Pilot
  Multi-Engine Commercial Rating
  Flying Since 2005
    Piper Seminole
    Beechcraft Duchess

## Slide 4: What is VMC
Defined Based on 14 CFR 23.149(a)
“VMC is the calibrated airspeed at which, when the critical engine is suddenly made inoperative, it is possible to maintain control of the airplane with that engine still inoperative, and thereafter maintain straight flight at the same speed with an angle of bank of not more than 5 degrees. The method used to simulate critical engine failure must represent the most critical mode of powerplant failure expected in service with respect to controllability.”

## Slide 5: Why is VMC Important?
VMC is the airspeed which if above will allow the aircraft to maintain directional control.
https://www.youtube.com/watch?v=ZBcvb400JgM

## Slide 6: Effects on Aircraft During Engine Failure
Pitch Down
  Due to the loss of induced airflow over the horizontal stabilizer
Roll towards dead engine
  Due to loss of accelerated slipstream over the dead engine wing
Yaw towards dead engine
  Due to the asymmetrical thrust situation
Climb performance decreased by 80%

## Slide 7: VMC Corrections
Bank 3-5 degrees into the good engine
  Lift vector is directed opposite to the yaw induced by the engine
  Reduces the amount of rudder required for directional control
  Feather the propellers (If available)

## Slide 8: Piper Seminole Fuel System
Engine Nacelle Tanks
  Two 55 Gallon Tanks
  100LL
  2 Engine Driven Pumps
  2 Electrically Driven Pumps
  Cross Feed System

## Slide 9: Piper Seminole Engine System
Lycoming
  2 x 180HP
  Piston Driven
  Horizontally Opposed
  Air Cooled
  Normally Aspirated
  Direct Drive
Propeller
  Twin Blade Metal Propellers
  Controllable Pitch
  Constant Speed
  Full Feathering

## Slide 10: Piper Seminole Propeller System

## Slide 11: Large Multiengine Aircraft Systems for Engine failure
Fuel System
  Shut off Values
  Fuel Dump
Pneumatic System
Hydraulic System
Fire System
  Fire Extinguishers

## Slide 12: Gulfstream G450 Fire System
Sensors
  7th and 12th stage in compressor
  At Bleed Air
  Inboard of the Engine
  Left Engine at anti-ice duct
Fire Extinguishers
  Two bottles located in the tail

## Slide 13: Gulfstream G450 Fuel System
Engines
  Rolls-Royce Tay-611-8c
  13,580 lbs thrust
Fuel
  2 Wing Tanks
  29,500 lbs.
  Series of pumps and lines to supply fuel to the engine

## Slide 14: Boeing 737 Fuel System
Three Fuel Tanks
  Two Wing tanks
  One Center Tank
6800 Gallons of Jet A
Cross Feed System
Shut Off Valves
No Fuel Dump System

## Slide 15: Boeing 737 hydraulic system
Two Hydraulic Systems
  Both engines power both systems
Standby system
Both Systems Control
  Autopilot
  Rudder PCU
  Elevator Actuators
  Aileron PCU

## Slide 16: Boeing 737 fire system
Two Fire Bottle’s for Engines
One Bottle for APU

## Slide 17: Boeing 747 Fire system operation
https://www.youtube.com/watch?v=ltMFvT6YxAM

## Slide 18: Case Study 1: TransAsia Flight 235
February 6th 2015, 10:52am
Aircraft
  ATR 72-600
List of Events
  Two Minutes After Takeoff Right Engine Failure Alert
  Pilots Reduce Power to Left Engine
  Stall Warning sounds
  Crew Cuts power to left engine
  Crew realizes mistake and starts the left engine
  Master Warning Sounds
  Plane Clips a bridge and crashes into a river

## Slide 19: Case Study 2: Delta Airlines Flight 295
September 21, 2014
Boeing 747
List of Events
  Aircraft was taking off at Hartsfield's-Jackson Airport
  At 400 ft. AGL the pilots heard a loud bang and the airplane yawed.
  Noted that engine 4 instrument indicated a loss of power
  Engine failure and shutdown completed for engine 4
  AT 1300 ft. AGL engine 4 fire warning activated

## Slide 20: Case Study 2: Delta Airlines Flight 295
List of events continued
  Pilots discharged A fire bottle into engine 4
  Fire warning remained illuminated for 1 minute
  Pilots discharged B fire bottle into engine 4
  Warning extinguished after 20 seconds
  Pilots dumped 280,000 lbs. and returned to airport

## Slide 21: Boeing 747 Fuel Dump
https://www.youtube.com/watch?v=Hn2gvinGKMg

## Slide 22: Questions?
Email: Mjporemba@Crimson.ua.edu